## Slide 1: Coil Gun
Zap

## Slide 2
Working Principles
Design Architecture
Safety Principles
Plan of Action

## Slide 3
Working Principles
Design Architecture
Safety Principles
Plan of Action

## Slide 4: Electromagnets
Magnets that turn on and off via current running through wire
Magnetic field generated via RHR
Thumb in direction of current -> fingers coil in B-field
Coil of wire has magnetic field produced strongest internally

## Slide 5: Magnetic Materials
Ferromagnetic
Attracted to both poles of a magnet, maintain magnetism after removal of external B-Fields
Paramagnetic
Attracted weakly to magnets, do not retain magnetism once B-field is removed
Diamagnetic
Repels magnets, does not retain magnetism once B-Field is removed

## Slide 6: Coil Attraction
Ferromagnetic and Paramagnetic Materials attracted to the center of solenoids
Diamagnetic materials repelled from centre of coils
The stronger the B-Field produced, the stronger the force
However, in isolation the materials get stuck in the middle of the coil for attractive forces, or can’t enter the coil in the first place for repulsive forces

## Slide 7: Coil Switching
This is why we use electromagnets instead of magnets
For attractive forces -> cut current after the projectile is past halfway point
For repulsive forces -> turn current on after projectile is past halfway point
Can be done with sensors or timers

## Slide 8: How to generate a strong B-Field?
B-Field Proportional to current and a few other properties
Shorting a wire gives maximum current (internal wire resistance)
For a given length of wire, a voltage has a maximum current
Increase the voltage!
Batteries and power supplies throttle current for protection
Solution? Capacitors!

## Slide 9: Capacitors
Charge caps to high voltage -> short caps through solenoid
Isn’t shorting Capacitors dangerous?
No! The coil is an inductor!

## Slide 10: Recap
High voltage capacitors are charged
Shorting the capacitors through coils produces strong B-fields
B-Fields attract/repel magnetic materials to towards/away their center
Sensors or timers are used to stop current flow and allow projectile to accelerate

## Slide 11
Working Principles
Design Architecture
Safety Principles
Plan of Action

## Slide 12: Coil Gun Subsystems
Chassis
Propulsion
Controls
Safety

## Slide 13: Chassis
Mechanical housing and mounting of all other subsystems
Ergonomic handling, projectile barrel, component housing, trigger, reload point
Coil and capacitor holder
Overall aesthetic design

## Slide 14: Propulsion
Coil parameters: number of windings, wire gauges, coil thickness, coil length
Capacitor selection
Capacitor charging circuit

## Slide 15: Controls
External sensors or timers for current cut
Voltage monitor
UI -> LEDs, LCD Screens,
Velocity monitor
Adjustable power level

## Slide 16: Safety
Capacitor discharge circuit
Mechanical capacitor discharge mechanism
Bleeder Resistor
Deadman’s switch
Testing Rig, remote firing mechanism

## Slide 17
Working Principles
Design Architecture
Safety Principles
Plan of Action

## Slide 18: 1. High voltage capacitors
Capacitors discharge almost instantaneously when shorted
Must stay under voltage rating
Polarity!
Reliable discharge methods, both mechanical and within system
Passive discharge
Video of capacitor short

## Slide 19: 2. Inductors
Instant current cutoff causes inductor kickback
Must include flyback diode

## Slide 20: 3. Component Ratings
All components in contact with HV wires need to be HV rated
Mechanical switches in series can fuse together at high voltages
Diode Breakdown voltages
uC ratings
HV can arc across small airgaps
Resistor W ratings

## Slide 21: Safety Implementation
Design
Bleeder resistors
Capacitor discharge circuit
Testing Rig
Remote firing for testing
Dead man’s switch
Design to fail open
Processes
Electrical gloves
Safety Glasses
Test outside
Regular gun safety
Checklist
Indirect voltage measurement -terminals

## Slide 22
Working Principles
Design Architecture
Safety Principles
Plan of Action

## Slide 23: Design Division
Chassis – CAD Design, Trigger mechanism, Deadman's switch, component mounting.
Propulsion – Coil length, width, number of turns, and wire gauge. Capacitor selection.
Controls – PCB design, Modularity, Speed sensing, UI (LCD screen, LEDS, variable power)
Safety – Checklist, capacitor discharge circuit, mechanical discharge device, test rig,

## Slide 24: Proposed Plan
Every meeting choose 1-3 things to complete for next meeting. If tasks are large/complex, further break down into individual tasks and choose
Record everything we do
Aim to have material ordered by Aug 2

## Slide 25: Bill of Materials
Projectile + extras
Barrel material
PCB and electronic components
HV capacitors
COTS charging circuit?
Sensors (speed, detection)
Housing Material (3D Print? Injection Molding? Vaccuum Molding? Custom Part order?)
Buttons, LEDS, LCDs
Wire for coils
Microcontroller
Sensors